## Slide 1
FINAL YEAR PROJECT · RESULTS REVIEW
Real-Time Adaptive Audio Noise Cancellation
Using Learning-Based Frequency-Domain Processing on Edge Hardware
+9.9 dB
SNR improvement
6 of 6
metrics beat all baselines
722 K
params · real-time
Guide: Dr. G. R. Venkatakrishnan
A Rohit Daniel · Simhaa TT · Vijayaraghavan A

## Slide 2
1 · THE PROBLEM
Traditional noise cancellation is fixed and blind
1
Manual tuning
Thresholds must be re-tuned by hand for every noise environment.
2
Amplitude-only
Removes components by loudness — no idea which bins carry speech.
3
Fails on real noise
Works only for stationary noise; struggles with non-stationary / burst noise.
4
Loses weak speech
Strips quiet speech components, hurting intelligibility.
MEASURED CONSEQUENCE
−3.7 to −5.8 dB
SI-SDR on real noise.
Classical DSP filters make the signal WORSE than doing nothing — they remove weak speech along with the noise.
Real-Time Adaptive Noise Cancellation · Results Review
2

## Slide 3
2 · OUR APPROACH
A model that learns which frequencies to keep
Instead of a fixed amplitude rule, a lightweight neural model looks at each frequency band in context and predicts how much to suppress it — learned from thousands of clean/noisy speech pairs.
✓
Context-aware
Uses band energy + spectral flux + past frames, not just loudness.
✓
Preserves weak speech
Keeps quiet speech bins that thresholding would delete.
✓
Adapts to any noise
Handles non-stationary and unseen noise types.
✓
Edge-ready
722 K params, runs in real time — deployable on-device.
Real-Time Adaptive Noise Cancellation · Results Review
3

## Slide 4
3 · SYSTEM PIPELINE
From microphone to clean audio — in real time
Noisy
audio in
Frame +
STFT
Band
features
Learned
model
Adaptive
mask
ISTFT +
overlap-add
Clean
audio out
16 kHz
sample rate
512-pt
STFT · 128 hop
32
Bark bands
722 K
model params
~64 ms
latency
Block-based streaming with overlap-add — the same path runs offline (files) and live (microphone).
Real-Time Adaptive Noise Cancellation · Results Review
4

## Slide 5
4 · CORE RESULT
Learned model vs classical baselines — same 824 clips
Method (VoiceBank-DEMAND test)
SI-SDRi ↑
STOI ↑
ESTOI ↑
LSD ↓
Noisy input (no processing)
0.0
0.921
0.787
10.50
Hard threshold
−3.69
0.767
0.573
13.78
Soft threshold
−5.82
0.728
0.532
15.28
Spectral subtraction
−0.25
0.884
0.734
8.86
Wiener filter
−1.93
0.824
0.677
10.87
Learned model (ours)
+9.93
0.930
0.832
6.47
THE ONLY METHOD
that improves the signal on every metric.
Every classical filter has NEGATIVE SI-SDR — they strip weak speech on real, non-stationary noise. The learned model gains +9.9 dB and lifts intelligibility.
↑ higher is better ↓ lower is better
Real-Time Adaptive Noise Cancellation · Results Review
5

## Slide 6
5 · SPEECH CLARITY
Classical filters denoise by damaging speech
Noisy
Best classical*
Learned (ours)
STOI (intelligibility)
0.921
0.884 ↓
0.930 ↑
ESTOI
0.787
0.734 ↓
0.832 ↑
PESQ (quality)
1.97
—
2.49 ↑
* spectral subtraction, the strongest classical baseline.
KEY INSIGHT
Every classical filter LOWERS intelligibility (STOI) below the untouched noisy signal — proof they remove speech, not just noise.
Only the learned model raises both intelligibility and quality.
Real-Time Adaptive Noise Cancellation · Results Review
6

## Slide 7
6 · REAL-TIME PERFORMANCE
Fast enough for live, on-device use
0.009
real-time factor
processes 1 s of audio in ~9 ms
~64 ms
algorithmic latency
block-based overlap-add streaming
> 100×
faster than real time
large headroom for edge hardware
Same real-time factor as the classical filters (~0.008) — the learned model adds no runtime cost while delivering far better quality. Target edge device: Raspberry Pi.
Real-Time Adaptive Noise Cancellation · Results Review
7

## Slide 8
7 · PROJECT STATUS
Progress against the objectives
✓
Real-time FFT pipeline
✓
Learned per-band suppression model
✓
Full mic → FFT → model → IFFT path
✓
Trained on clean/noisy pairs (VoiceBank + MS-SNSD)
✓
Benchmarked vs 4 classical baselines
✓
SNR, spectrum, clarity, latency measured
✓
External validation on unseen noise (MS-SNSD: +3.2 dB)
→
Edge deployment on Raspberry Pi
→
Live microphone demo
→
Word Error Rate (ASR) evaluation
Real-Time Adaptive Noise Cancellation · Results Review
8

## Slide 9
8 · NEXT STEPS & FUTURE SCOPE
From benchmark to on-device product
IMMEDIATE
Deploy quantized model on Raspberry Pi
Live mic → speaker demo with latency check
Add WER evaluation with an ASR model
FUTURE SCOPE
Hearing aids — profile-tuned suppression
Video conferencing & smart speakers
Live broadcast / podcast noise cleaning
Bottom line: a learned adaptive filter that beats every classical baseline on real noise, at real-time speed — ready to move onto edge hardware.